## Slide 1
Sampled telemetry and
adaptive flood detection
A controlled 5G-NIDD replay study in an SDN emulator
54 accepted live trials
Independent packet truth and reproducible measurements
Notes: Official dataset: https://arxiv.org/abs/2212.01298 and https://doi.org/10.23729/e80ac9df-d9fb-47e7-8d0d-01384a415361. Existing HAT/ADWIN and sFlow methods; no new algorithm or physical 5G claim.

## Slide 2
Study design
M3 controlled replay study 2
Six switch sampling values: N = 1, 2, 5, 10, 20 and 50. Three repeats for each scenario and N.
Baseline, held-out SYN introduction, and a constructed family/cadence shift. Every selected class replays at 100 packets/s.
Primary windows: 0.1 seconds. A separate one-second sensitivity rebuilds features from saved raw exports.
N = 1 is the unsampled M3 reference. M1/M2 and automatic mitigation are outside this study.
Notes: Source: configs/research_protocol.json, frozen before primary outcomes. Local protocol, not an external preregistration registry.

## Slide 3
Independent truth and causal prediction
M3 controlled replay study 3
Sender and receiver captures agree on every original frame. Kernel receive timestamps define physical attack onset.
The detector predicts before reading that window’s independent label. Scoring precedes learning.
The 0.5-second parameter holds a completed window before prediction. The oracle label is then read immediately.
Empty sampled windows remain scored when original-packet truth exists. Unknown original truth stays unscored.
Notes: Sources: docs/research-methods.md; sdn/live_ground_truth.py; src/m3/causal_live.py. sFlow specification https://sflow.org/sflow_version_5.txt. Labels derive from authoritative original flow matches, not filenames or sampled predictions.

## Slide 4
Mean attack F1 by sampling rate
M3 controlled replay study 4
Chart: Switch sampling denominator N
| 1 | 2 | 5 | 10 | 20 | 50
Baseline | 0.69192 | 0.95624 | 0.77726 | 0.68779 | 0.60058 | 0.61477
Drift | 0.77783 | 0.95403 | 0.77648 | 0.70179 | 0.61416 | 0.61431
Unseen | 0.68802 | 0.96179 | 0.77673 | 0.70933 | 0.63017 | 0.59481
Trial means. Sample SD and unbounded 95% Student-t intervals are in the report.
Notes: Source: research/results/aggregated_metrics.json and linked primary run evidence. Three repeats per cell; fixed traffic, limited generalization.

## Slide 5
Measured control-channel cost
M3 controlled replay study 5
Chart: Switch sampling denominator N
| 1 | 2 | 5 | 10 | 20 | 50
Baseline | 160.1318 | 84.8108 | 39.9415 | 24.8193 | 17.5682 | 13.0501
Drift | 141.3185 | 76.2327 | 36.3451 | 23.0919 | 16.5321 | 12.7757
Unseen | 159.2934 | 85.1641 | 39.8534 | 24.8491 | 17.7295 | 12.9534
Trial means. Sample SD and unbounded 95% Student-t intervals are in the report.
Notes: Source: research/results/aggregated_metrics.json and linked primary run evidence. Three repeats per cell; fixed traffic, limited generalization.
Cost basis: sFlow IPv4+UDP+payload; OpenFlow captured IP bytes. Full combined-channel Pareto analysis is in the report. No physical wire/FCS or switch-CPU claim.

## Slide 6
False positives remain visible
M3 controlled replay study 6
Chart: Switch sampling denominator N
| 1 | 2 | 5 | 10 | 20 | 50
Baseline | 0.88671 | 0.08963 | 0.47308 | 0.70959 | 0.82026 | 0.76098
Drift | 0.62867 | 0.095094 | 0.48844 | 0.72592 | 0.90572 | 0.92244
Unseen | 0.90102 | 0.077224 | 0.49433 | 0.7188 | 0.91226 | 0.85407
Trial means. Sample SD and unbounded 95% Student-t intervals are in the report.
Notes: Source: research/results/aggregated_metrics.json and linked primary run evidence. Three repeats per cell; fixed traffic, limited generalization.

## Slide 7
Physical detection and recovery
M3 controlled replay study 7
Baseline
N=1: 0.635 s, 3/3 detected N=50: 1.201 s, 3/3 detected
Drift
N=1: 0.629 s, 3/3 detected N=50: 1.368 s, 3/3 detected
Unseen
N=1: 0.597 s, 3/3 detected N=50: 1.287 s, 3/3 detected
Drift recovery at N=2: 6.506 s, 3/3 recovered with the fixed criterion.
First post-warm-up attack episode. Means include detections only; misses are censored, never zero.
Notes: Source: research/results/aggregated_metrics.json and linked primary run evidence. Three repeats per cell; fixed traffic, limited generalization.

## Slide 8
Previously held-out SYN family
M3 controlled replay study 8
Chart: Switch sampling denominator N
| 1 | 2 | 5 | 10 | 20 | 50
SYN recall | 0.99588 | 0.99725 | 0.97521 | 0.95199 | 0.89957 | 0.81323
SYN is absent during warm-up. Subsequent oracle labels allow adaptation, so this is not a broad zero-day guarantee.
Notes: Source: research/results/aggregated_metrics.json and linked primary run evidence. Three repeats per cell; fixed traffic, limited generalization.

## Slide 9
Descriptive sampling recommendations
M3 controlled replay study 9
Drift: N=2
Mean F1 0.954 and combined IP cost 76.724 kbit/s
Baseline: N=2
Mean F1 0.956 and combined IP cost 85.134 kbit/s
Unseen: N=2
Mean F1 0.962 and combined IP cost 85.635 kbit/s
Fixed equal-weight distance to the normalized ideal. These are in-study suggestions, not universal optima.
Notes: Source: research/results/aggregated_metrics.json and linked primary run evidence. Three repeats per cell; fixed traffic, limited generalization.

## Slide 10
Evidence, limits and demonstration
M3 controlled replay study 10
Reproduce from the official dataset, frozen protocol, source mappings and trial configurations. Failed attempts remain recorded.
The report includes paired uncertainty, nonadaptive-tree and majority ablations, and one-second sensitivity.
Constructed timing, flow correlations, oracle labels and one shared-host emulator limit generalization. No physical 5G deployment claim.
Demo: open the local dashboard, choose a validated live trial, inspect predictions and cost, then compare compatible N values.
Notes: Source files: research/M3_Research_Report.md, docs/research-methods.md, docs/research-related-work.md, research/results/derived_trial_evidence.zip. HAT: https://doi.org/10.1007/978-3-642-03915-7_22. ADWIN: https://doi.org/10.1137/1.9781611972771.42. Prior sampling study: https://doi.org/10.1016/j.future.2019.10.015.